## Slide 1
DISASTER INTELLIGENCE PLATFORM
NER-LEWS
North Eastern Region Landslide Early Warning System
An AI & Rule-Based Multi-Hazard Early Warning and Decision Support Platform for Northeast India
PLATFORM OVERVIEW
• Domain: Landslide Hazard Early Warning & Zonation
• Architecture: Web-GIS & Rule-Based MCDA Engine
• Coverage: 8 North Eastern States (NER India)
• Key Corridors: NH-6, NH-54, NH-29, NH-10 Transit Lines
• Live App: https://ner-lews.vercel.app/
• REST API: https://ner-lews.onrender.com/

## Slide 2
EXECUTIVE SUMMARY: THE NER-LEWS PLATFORM
Real-Time Slope Monitoring, Transparent Scoring & Multilingual Alerts
2
NER-LEWS | Disaster Risk Reduction Platform | Live App: https://ner-lews.vercel.app/
🚨 The Problem & Solution Architecture
• Severe Monsoons: Heavy rainfall (>2500mm/yr) causes slope destabilization across Eastern Himalayas.
• Highway Blockages: Essential transit lifelines (NH-6, NH-54) cut off entire state supplies for days.
• Transparent MCDA Scoring: Evaluates 5 physical parameters without unexplainable black-box ML.
• Interactive Web-GIS Map: Real-time telemetry monitoring for 10+ stations with radar hazard pins.
• Multilingual Voice Alerts: Native browser voice synthesis in English, Assamese, Hindi, and Bengali.
• Citizen Geotagged Reports: Crowdsourced GPS photo evidence with auto-sync to SDMA.

## Slide 3
TECHNICAL ARCHITECTURE & RISK FORMULA
End-to-End Technology Stack, Multi-Criteria Algorithm & Data Pipeline
3
NER-LEWS | Disaster Risk Reduction Platform | Live App: https://ner-lews.vercel.app/
📐 Geotechnical Risk Scoring Formula
Step 1: Normalization to 0-10 Sub-Scores:
• 24h Rain: 0mm→0 | 50mm→3 | 100mm→6 | 150mm+→10
• Soil Moisture: 0% to 100% linear (0-10)
• Elevation: 0-500m→2 | 500-1500m→5 | 1500-2500m→8 | 2500m+→10
• Humidity: 0% to 100% linear (0-10)
• Temperature Modifier: <15°C or >30°C adds +0.5 penalty
Step 2: Weighted Sum Calculation:
Final Score = (Precip × 0.35) + (Soil × 0.30) + (Elev × 0.20) + (Hum × 0.15) + TempMod
Step 3: 4 Severity Risk Bands:
• 0.0 – 3.0: LOW RISK (Green) -> Routine monitoring
• 3.1 – 6.0: MODERATE RISK (Yellow) -> Field officer inspection
• 6.1 – 8.0: HIGH RISK (Orange) -> Road advisory & alerts
• 8.1 – 10.0: SEVERE RISK (Red) -> Immediate evacuation advisory

## Slide 4
FEASIBILITY, CHALLENGES & MITIGATION
Operational Viability, Hill Terrain Obstacles and Engineering Solutions
4
NER-LEWS | Disaster Risk Reduction Platform | Live App: https://ner-lews.vercel.app/
📊 Feasibility Analysis & Practical Solutions
• Technical Viability: 100% built and live in production; sub-second page loads on 3G/4G.
• Financial Feasibility: Eliminates proprietary GIS and TTS licensing fees; zero operational server cost on free tier.
• Hill Connectivity: Client-side offline evaluation engine and seed caching keep alerts functional without network.
• Regional Languages: Native browser voice synthesis in Assamese, Bengali, and Hindi with regional dialect mappings.
• Hardware Gaps: Citizen hazard crowdsourcing with geotagged photo proof bridges sparse sensor networks.

## Slide 5
IMPACT, BENEFICIARIES & AUDIO ADVISORIES
Social, Economic, and Disaster Risk Reduction (DRR) Benefits for Northeast India
5
NER-LEWS | Disaster Risk Reduction Platform | Live App: https://ner-lews.vercel.app/
👥 Public Safety & Economic Preservation
• Early Evacuation Time: 6 to 24 hour prescriptive warning window before slope saturation triggers rupture.
• Universal Accessibility: Multilingual voice advisories ensure illiterate, elderly, and rural citizens receive alerts.
• Highway Transit Preservation: Prevents multi-day supply chain blockages along NH-6, NH-54, and NH-29.
• Targeted Resource Dispatch: Empowers SDRF & District Magistrates with pinpointed hazard sector intelligence.
• Aligned with Sendai Framework: Directly supports global DRR Target G (Multi-hazard early warning systems).

## Slide 6
RESEARCH GROUNDING & AUTHORITY DASHBOARD
Geotechnical Basis, Authority Portal & Live Production Deliverables
6
NER-LEWS | Disaster Risk Reduction Platform | Live App: https://ner-lews.vercel.app/
📚 Scientific Grounding & Live Links
• GSI Guidelines: National Landslide Susceptibility Mapping (NLSM) for Himalayan terrain.
• IMD Research: Rainfall intensity-duration thresholds for slope failure initiation in Meghalaya & Mizoram.
• NESAC / ISRO: Early Warning Methodologies and rainfall zonation in East Khasi Hills.
• Web Application: https://ner-lews.vercel.app/ (Live on Vercel)
• REST API Server: https://ner-lews.onrender.com/ (Live on Render)
• Development: UI/UX structured with Stitch; full-stack engineered with Google Antigravity AI.